## Slide 1
3M · INTERNSHIP PROJECT PROGRESS
AI Yoga Posture
Correction System
A live background coaching system that watches you do yoga, compares your pose to the instructor, and tells you exactly what to fix.
Progress Report

## Slide 2
What Was Built
A fully modular, real-time pose correction pipeline — 19 Python files running live on Windows.
19
Python modules
3,500+
Lines of code
18
Yoga pose classes
98.7%
ML classifier acc
webcam_capture
Webcam input
screen_capture
Screen / video input
pose_estimator
MediaPipe landmarks
angle_calculator
Joint angle math
pose_classifier
ML + rule-based classify
similarity_scorer
Weighted pose scoring
ghost_skeleton
Body stencil overlay
feedback_builder
Natural voice cues
pose_state_machine
Hold / freeze logic
session_tracker
Session summary
Project Overview
All modules fully integrated + running live

## Slide 3
Dual Capture System
Captures the user via webcam AND the instructor from any on-screen video — simultaneously.
📷 Webcam Capture
▸ OpenCV VideoCapture — auto-selects device index
▸ 640×480 @ 30 fps, index configurable via --webcam flag
▸ Auto-reconnect loop on dropped frames (3 s retry)
▸ Camera checker: warns if body cut off, sideways, too small, or too close
▸ Sideways detection: X-separation < 0.06 AND Y-diff > 0.12 (dual condition)
🖥️ Screen Capture
▸ mss library captures full monitor at 5 FPS
▸ Auto-detects black frames caused by GPU-accelerated video
▸ Fallback: Win32 BitBlt via pywin32 for DRM/GPU content
▸ DPI awareness registered before any Win32 API calls
▸ Supports 2560×1600 high-DPI displays
▸ Monitor index configurable via --monitor flag
⇄
live
Dual Capture System
GPU video fallback fully working on Windows

## Slide 4
Pose Estimation — MediaPipe
33 3D landmarks extracted per frame, filtered by visibility, converted to joint angles.
How It Works
▸ MediaPipe Pose processes each frame at 5 FPS
▸ Returns 33 landmarks: (x, y, z, visibility) per point
▸ Visibility threshold 0.55 — unreliable points ignored
▸ Coordinates normalised 0.0 → 1.0 (frame-relative)
▸ Runs independently on both webcam and instructor stream
▸ Dataclasses: PoseResult → dict[name, Landmark]
10 Joint Angles Computed
Left Knee
Hip → Knee → Ankle
Right Knee
Hip → Knee → Ankle
Left Hip
Shoulder → Hip → Knee
Right Hip
Shoulder → Hip → Knee
Left Shoulder
Elbow → Shoulder → Hip
Right Shoulder
Elbow → Shoulder → Hip
Left Elbow
Shoulder → Elbow → Wrist
Right Elbow
Shoulder → Elbow → Wrist
Left Ankle
Knee → Ankle → Foot
Right Ankle
Knee → Ankle → Foot
Pose Estimation — MediaPipe
Both streams processed every 0.2 s

## Slide 5
Pose Similarity Scoring
Every frame produces a 0–100% match score comparing user angles to instructor angles.
Score Formula
score = Σ weight_j × max(0, 1 − |user_angle_j − ref_angle_j| / 180) × 100
< 60%
Needs Work
60–75%
Fair
75–85%
Good ✓
85–100%
Excellent ✓✓
Hold Detection
▸ User must sustain ≥ 75% score for 8 continuous seconds
▸ Progress arc drawn in debug window (fills as timer runs)
▸ Score drops below threshold → timer resets to zero
▸ On success: 'Well done!' spoken + session records the hold
Joint Weights
Hips / Knees
Weight ×1.5 (load-bearing joints)
Shoulders
Weight ×1.2 (arm position)
Elbows
Weight ×0.9
Ankles / Wrists
Weight ×0.7 (extremities)
Pose Similarity Scoring
Hold threshold: 75% · Hold duration: 8 s

## Slide 6
ML Pose Classifier — 98.7% Accuracy
Custom-trained Random Forest on 7,200 synthetic samples — auto-loads at startup.
Trained Model
▸ Random Forest — 200 estimators, sklearn Pipeline + StandardScaler
▸ 7,200 synthetic samples (400 per pose × 18 classes)
▸ 24 input features: 12 joint angles + 12 derived features
▸ Derived: bilateral symmetry diffs, knee/hip ratios, bilateral means
▸ Confidence gate: rejects predictions below 45% probability
▸ Fallback to rule-based constraint scorer if model absent / uncertain
▸ Auto-loaded from model/pose_classifier.pkl at startup
18 Pose Classes Recognised
Mountain
Forward Fold
Halfway Lift
Warrior I
Warrior II
Warrior III
Chair
Tree
Triangle
Downward Dog
Plank
Low Lunge
High Lunge
Cobra
Upward Dog
Child's Pose
Seated Forward
Cat-Cow
ML Pose Classifier
13/13 manual test cases passing · 98.7% test accuracy

## Slide 7
Body Stencil Overlay (ghost_skeleton.py)
The instructor's silhouette is drawn colour-coded directly over the user's webcam feed.
How It's Rendered
▸ Each limb segment rendered as a filled capsule (thick rounded shape)
▸ White glow outline drawn first for visibility on any background
▸ Body-aligned: scaled to user's torso height, anchored to user's hips
▸ Stencil drawn at 42% opacity — webcam remains visible underneath
▸ User's own skeleton drawn in white on top of the stencil
▸ Joint dots with colour ring drawn over every landmark
▸ Segments: upper arm, forearm, thigh, shin, torso (both sides)
Live Colour Coding (per joint + segment)
Matched
Angle within ±20° tolerance
Close
Within ±40° (2× tolerance)
Adjust
Within ±60° (3× tolerance)
Fix This
Beyond ±60° — clear misalignment
No Data
Instructor joint not visible
Body Stencil Overlay
Scales + translates to match user's body size in real-time

## Slide 8
Natural Voice Coaching (feedback_builder.py)
Pose-specific, severity-scaled corrections spoken aloud in real time — not robotic commands.
TTS Engine:
Primary: edge-tts (en-US-JennyNeural) → Fallback: pyttsx3 → OS subprocess → console print
Non-blocking audio queue — never stalls the pose loop. pyttsx3 init in worker thread (fixes Windows COM hang).
Feedback Design
▸ Pose-specific language: Warrior II cues ≠ Chair Pose cues
▸ Severity-scaled: diff >35° → direct; diff <15° → soft suggestion
▸ Combined sentences when 2 joints mismatch simultaneously
▸ Encouragement probability scales with closeness to target
▸ 6-second cooldown between corrections (never overwhelming)
▸ 8+ phrase variants per joint/direction to avoid repetition
Example Voice Lines
Warrior II knee:
"Warrior Two lives in the legs — sink deeper into that left knee, directly over your ankle."
Both arms:
"Sweep both arms up — reach them overhead."
Close correction:
"Straighten your right leg — press the heel down. Almost there."
Pose intro:
"We're going into Downward Dog now, Adho Mukha Svanasana."
Well done:
"That's it — hold that and breathe."
Natural Voice Coaching
Pose-aware · Severity-scaled · Cooldown-gated

## Slide 9
State Machine & Session Tracking
Finite state machine governs pose transitions. Every session ends with a spoken summary report.
TRACKING
FROZEN
CATCHING UP
Instructor moves on →
→
User holds 8 s →
→
Transition Rules
▸ Hold = score ≥ 75% continuously for 8 seconds
▸ Instructor pose confirmed after 4 consecutive frames (~0.8 s)
▸ Unknown / 'Yoga Pose' frames never trigger transitions
▸ FROZEN: orange banner shown, step-by-step cues continue
▸ Score bands: Excellent 85% / Good 75% / Fair 60% / Work <60%
Session Summary (session_tracker.py)
▸ Records: held / missed per pose, best score, time spent
▸ End-of-session summary spoken aloud automatically
▸ Terminal table printed with per-pose breakdown
▸ Voice commands: score · what pose · next step · pause · resume
▸ Keyboard: Q quit · S score · N next step · P pause · R repeat
State Machine & Session Tracking
States: TRACKING → FROZEN → CATCHING UP

## Slide 10
Progress Summary — What's Complete
2025
✓
Webcam capture + camera alignment checker
✓
Screen capture with GPU/BitBlt fallback
✓
MediaPipe pose estimation (both streams)
✓
10 joint angles computed per frame
✓
Weighted cosine similarity score (0–100%)
✓
18-class ML classifier — 98.7% accuracy
✓
Custom training pipeline + live recording mode
✓
Rule-based fallback classifier (13/13 tests pass)
✓
Body stencil overlay — colour-coded, body-aligned
✓
Natural voice coaching — pose + severity aware
~
Voice command recognition (needs pyaudio)
○
Kaggle real-data fine-tuning (optional)
10/10
Modules built
98.7%
ML accuracy
18
Pose classes
Live
Running on Windows